## Slide 1: Virtual Numpad using EMG Signals
~ Vinita Narayanamurthi
Rashmi Ballamajalu

## Slide 2: Motivation EMG signals -> gestures done using fore, middle and ring fingers
Myo armband used to build a virtual number pad
Current implementations using camera, light/shadow sensors, and software keyboards that use mouse click
Use of bio signals induce challenges in generalizing trained model
Advantage -> Myo armband is the only hardware required

## Slide 3: Implementation
Raw EMG Signal of Finger Movements using MYO Armband
Event Marker Random Number generator (0-9)
Data Acquisition using Lab Stream Layer
Pre-Processing (Zero Mean & 60 Hz Noise Removal using Butterworth Filter)
Feature Extraction
Classification Using SVM And Decision Tree
Features Extracted
Root Mean Square (RMS) deviation of the signal
Variance
Difference Absolute Standard Deviation (DAS) of wavelength between consecutive samples
Maximum Fractal Length -> for measuring low-level signals
Average Amplitude Change -> contains information about frequency, duration and amplitude of signal

## Slide 4: Training Model and Results
Scatter Plot
Offline Accuracy
Bias reduced -> model trained with data points randomized
Data collected over multiple days

## Slide 5: Real Time Implementation
Raw EMG samples collected -> window of 3s (~600)
Data Acquisition using Lab Stream Layer
Pre-Processing
Feature Extraction
Classification Using Trained Model
Show output to user through GUI

## Slide 6: Real Time Misclassification Confusion Matrix Arm Muscles

## Slide 7: Future Work Questions
Generalize model to work for all
Improve reliability of model for faster typing speeds
How did we manage to reduce the bias while training the model.
As a customer, would you prefer a wearable sensor or a generic sensor like camera